## Slide 1: Surface Safety
Airfield Movement Areas
OHIO AVIATION ASSOCIATION
Christine Madden Deputy Regional Administrator (A) Great Lakes
August 23, 2021

## Slide 2: Overview
Surface Safety – Best Practices
Construction ‘Tools’
Voluntary Reporting
Free Resources

## Slide 3: Runway Incursion “any occurrence in the airport runway environment involving an aircraft, vehicle, person, or object on the ground that creates a collision hazard or results in a loss of required separation with an aircraft taking off, intending to take off, landing, or intending to land.”

## Slide 4
Vehicle/Pedestrian Deviations (VPDs)
Runway Incursions are grouped into Surface Events
  A surface event caused by a vehicle driver or pedestrian on the movement area is a VPD
Notes: Mowers, snowplows, ARFF, police, POVs, tugs, Ops, Aircraft Mx Taxi, i.e., an not intended for flight and it is necessary to reach out to air carriers and corporate facilities.

## Slide 5: Best Practices Communication
Individuals have expressed that they are not comfortable talking to ATC
Training is essential!
Tips from FAA Office of Airports…
Notes: Ensure airport operators, anyone with a need to drive or walk within the confines of the Runway Safety Area (RSA), has been thoroughly trained on signs, markings, lighting, phraseology, radio usage, reading an airport diagram, and both day and night operations.
Use of proper phraseology
Listen & reply to ATC

## Slide 6: Best Practices Communication with ATC
Phraseology
  ROGER is not a clearance
    Actual Event – VPD occurred when an air traffic controller responded “ROGER” to a runway access request
Deviating from a clearance
  If you request to cross a runway and see FOD along the way, prior to deviating, you must contact the Tower and request a new clearance to the area with FOD, as well as to exit the vehicle
Notes: ROGER− I have received all of your last transmission. It should not be used to answer a question requiring a yes or a no answer.
Yes is AFFIRMATIVE and No is NEGATIVE

## Slide 7: Best Practices Special Events, Airshows & Tenant Events
Recommend additional oversight by airport operator
Train personnel for special events and/or have additional staff on hand to provide escorts
Tenants bringing guests to hangar areas (i.e., for a BBQ) should provide a short safety briefing on where they can and cannot go

## Slide 8: Best Practices Escorting
Ensure English Language Proficiency
  Prior to escorting anyone on the airfield
    Have a face to face conversation
    Ensure that you can clearly communicate
Brief the individual being escorted to
  Never pass the escort vehicle, even if they recognize their jobsite
    Actual Event – a VPD occurred during an escort to the construction site when the escort vehicle was instructed by ATCT to hold short, however the vehicle being escorted recognized the job site and went around the escort vehicle, and crossed the runway without a clearance
Give a printed handout to those who you are escorting
  Contact information for when they have to leave the site
  A better practice is to stay with the person/vehicle being escorted

## Slide 9: Best Practices Situational Awareness
Heads Up – Eyes Out
Eliminate Distractions
Use Airport Diagram
Listen to all radio calls
Be familiar with day & night operations
https://www.youtube.com/watch?v=gTc-SZi9nk8

## Slide 10: Best Practices Construction
Ensure all contractors & subcontractors are briefed
Provide oversight when haul roads or normally used service road routes change
  Additional signage/personnel monitoring the change
Use numbered maps with the depicted haul route
  Provide new maps when the haul route changes
  Ensure all maps are returned from the old route
Notes: Seasonal Tips – Construction
FAQs – Construction
CNDs – Currently this is a manual process. We expect to go to automated CNDs this Fall. Once this happens, an airport operator will need to use NOTAM Manager to create a CND when they enter a NOTAM into the system. If an airport is NOT on NOTAM Manager, they would not get a CND.
Runway/Taxiway Best Practices & Lessons Learned – a variety of airports provide information that is listed in this document.

## Slide 11
Notes: August 3, 2008 at 1519 a Cessna Citation 550
Day (1519L), VMC, dry, both cleared to land/cross by ATC. Cessna Citation struck the tractor with the left wing approximately 10 feet inboard from the wing tip. The wing was torn from the aircraft resulting in an aircraft fuel spill and significant damage to the aircraft and the tractor. There were no injuries or fire.
file:///C:/Users/Christine%20Madden/Downloads/ATC%203%20-%20Factual%20Report%20of%20Group%20Chairman-Master.PDF

## Slide 12: Accident…
Notes: August 3, 2008 at 1519 a Cessna Citation 550
Day (1519L), VMC, dry, both cleared to land/cross by ATC.
Cessna Citation struck the tractor with the left wing approximately 10 feet inboard from the wing tip.
The wing was torn from the aircraft resulting in an aircraft fuel spill and significant damage to the aircraft and the tractor.
There were no injuries or fire.

## Slide 13: Airfield Safety - Towered & Non-Towered Airports
Training focal points:
  Signs, Markings & Lighting (Day and Night)
  Phraseology
  Vehicle Walk-Around, Lights & Radios Working
  Airport Diagrams (Frequencies/Route/Hot Spots)
    Use Service Roads Where Possible
  Eliminate Distractions
  Heads Up – Eyes Out
  Look Both Ways Before Crossing
  Aircraft Landing Lights On? Likely Ready to Depart
Tips for a Towered Airport
Write the clearance
Understand the clearance
Clarify the clearance (if necessary)
Reply to the clearance
Know Light Gun Signals
Take radio when outside of the vehicle
Flash lights if radio is inoperable
https://www.faa.gov/airports/runway_safety/media/Ground_Vehicle_Guide_Proof_Final.pdf
Notes: Day and night training
Signs, markings and lighting
Airport diagrams (frequencies, hot spots, construction)
Radio and lights are operational
Proper phraseology
Use service roads whenever possible
Eliminate distractions, i.e., cell phone, passengers, etc.
Heads up – Eyes out
Look both ways, ensure there is no conflicting traffic
Be aware that an aircraft with landing lights is ready to depart
ATIS

## Slide 14: Construction
Seasonal Tips
Frequently Asked Questions
Construction Notice Diagrams
Runway & Taxiway Best Practice & Lessons Learned
FAA NOTAMS
Notes: Seasonal Tips – Construction
FAQs – Construction
CNDs – Currently this is a manual process. We expect to go to automated CNDs this Fall. Once this happens, an airport operator will need to use NOTAM Manager to create a CND when they enter a NOTAM into the system. If an airport is NOT on NOTAM Manager, they would not get a CND.
Runway/Taxiway Best Practices & Lessons Learned – a variety of airports provide information that is listed in this document.

## Slide 15: Construction Reminders
Collaborate – Communicate – Coordinate
  Air Traffic Manager (if towered)
  Airport Tenants
  Airport Users
Notes: Tell story about the airport operator who started construction on the airfield closing one of two runways, crossing runways. The longer runway was closed and airport tenants and users were unable to fly their aircraft into or out-of the airport. This can be avoided by communicating with your stakeholders, air traffic manager, tenants with flight departments, FBOs (transient aircraft).
Collaborate and communicate early and often, starting with the initial phase of project planning.
This concept may seem intuitive, however this happens often and it does not have to. Please consider impacts to the operation when planning construction projects. Success is hinged on collaboration, communication and coordination.

## Slide 16: Runway Safety Action Team (RSAT)
Local RSAT is led by the Tower Air Traffic Manager (ATM)
Must include the ATM and Airport Operator, at a minimum
Involve personnel from FAA lines of business, airport tenants & users
Convenes at least once per fiscal year
Discuss topics related to surface safety
Review & update the Runway Safety Action Plan (RSAP)
Be Involved

## Slide 17: RSAT Topics
Letters of Agreement (LOA)/published notices
Surface events
Mitigations
Construction
Hot Spots
Persistent weather issues
Action items
Best Practices/Lessons Learned
Wildlife
User concerns/feedback
Special Events
Notes: We now have an RSAT Web Tool which provides a visual graphic of the locations of runway incursions, excursions,

## Slide 18: How Do Pilots Get Information?
NOTAMs - Notices to Airmen
ATIS (Automated Terminal Information System)
Charting Publications
Hot Spots
Construction Notice Diagrams
Notes: Thinking about the information that a pilot needs to know when flying in/out of the airport environment, not limited to surface safety. This point serves as a reminder to work with the Tower Air Traffic Manager to coordinate communications to the airport users.

## Slide 19: Reporting
Towered Airports
  Mandatory Occurrence Reporting (MOR) process
  Ensure you are notified immediately when a VPD is filed for airport operations personnel
  Voluntary reporting is encouraged
Non-Towered Airports
  Data is only collected via voluntary reporting
https://asrs.arc.nasa.gov/index.html

## Slide 20: ASRS Examples
Light Transport Captain reported making a wrong turn during taxi at ### airport, citing poor signage as contributing.
Pilot reported a non-towered airport's publications and ASOS broadcast have not been updated to reflect a recent name change, with the inconsistency in naming causing NMAC events.
Reporter stated Taxiway A is not properly charted in the current NACO and Jeppessen diagrams and led to a Runway Incursion.
Tower Controller reported [multiple] aircraft having confusion with ### taxiways, resulting in frequent deviations from taxi instructions.
On approach with the FMS programmed and engaged. …GPWS [alerted] "too low terrain, pull up”…VMC with no terrain concerns. I am concerned that the top of the trees may be interfering with the approach clearance area. Also, taking off has resulted in a momentary GPWS warning when below 500 feet during climb.
Notes: UAS sitings, signage issues, NOTAMS,

## Slide 21: Outreach & Education - Drivers
FAA Runway Safety
Articles
  Construction
  Construction Best Practices_Lessons Learned User Feedback
  Construction Notice Diagrams
  Winter Ops
Videos
  Situational Awareness
  Phraseology – Coming soon!
  Signage – Coming Soon!
  FAA Summer Series - NOTAMS

## Slide 22: Outreach & Education - Pilots
FAA Runway Safety
From the Flight Deck Airport Specific and Single Topic Videos
Runway Safety Pilot Simulator
Free
Resources

## Slide 23: Outreach & Education Pilots